## Slide 1: Practical Winlink
With
Gerry Brown KK7GAB & Craig Cherry N7RWB

## Slide 2: What we will cover
Presentation
  What is WinLink
  Transports
  WWW Resources
  WinLink Express Application
Demo
  Download and Install VARA FM
    VARA FM Session
  MobiLinkD AX25 Session (If time available)

## Slide 3: What is WinLink
WinLink is an ecosystem of Client and Server applications that allow us to send emails
over amateur radio.
They can be sent from/to ham radio accounts or Internet email accounts
It supports attachments such as pictures and forms within size limits.
Connections can be Point to Point or via Internet Servers.
It is controlled by a team of developers that work with ham radio operators to enhance
the products as new technologies are developed. Updates are automatic through the
different applications that make up the ecosystem
Today we concentrate on “WINLINK EXPRESS”, the standard Windows client application.

## Slide 4: What are the Transports We Use?
Think of a transport as how we get from point A to point B.
When we go to the store we can:
1) Walk
2) Ride a bike
3) Take a bus
4) Drive a car
Similarly, we can use different transports to connect to WinLink Servers,
known as RMS (Remote Message Servers)
Some are slower and some are faster (technological advances)
Today we will discuss two transport mechanisms
AX25 and VARA
They require the use of a “soundcard” The soundcard changes the data into
tones that can be transmitted/received on amateur radios.

## Slide 5
AX25
Originally developed in the 1970s for amateur radio.
Based on the successful X.25 protocol used in data communications.
It supports packetization, and windowing:
Packets are fixed length objects with error detection
Windowing allows a numbering system of fixed size windows
E.G.
Side1 has sent 3 packets. And is sending the 4th
Side 2 has only received 2 packets
When Side 2 receives the 4th packet that says, “Here is packet 4”,
it replies. I expected to receive 3
Side 1 than resets its numbering and sends 3, then 4.

## Slide 6
VARA FM
Developed in 2020 by a Spanish programmer.
It uses packets and windows. BUT it adds signal processing techniques to
improve weak signal operation and digipeaters.
It is proprietary and requires a one time fee of $75 to use at full speed.
(Source code is held in an Escrow Account)

## Slide 7: Comparative Transport Speeds
Mode | Typical Throughput
AX.25 (1200) | 300–600 bps
AX.25 (9600) | 2–4 kbps
VARA FM (PAID) | 5–20 kbps
VARA HF (PAID) | 1–7 kbps (adaptive)
PACTOR 3/4 | 3–10+ kbps
In 2024, the FCC allowed for faster digital symbol rates leading
to faster VARA and PACTOR 4

## Slide 8
TNCs Terminal Node Controllers
A KISS TNC converts digital data to sounds. Also known as a SoundCard
The ones we use:
AX25: Kantronics KPC3+
MobiLinkD
VARA: Masters Communicatioms DRA-50M
Tigertronics SignaLink USB

## Slide 9
C
TNC
SoundCard
WinLink
Express
Transport
Vara/AX25
Amateur
Radio
Computer

## Slide 10
Kantronics KPC3+ for AX25
Kantronics KPC3+ $249
10 Pin Yaesu Cable $ 70
Total $319

## Slide 11
Common TNC for VARA
Tigertronics SignaLink USB
SLUSB6OM $120
Jumper Block $ 9
Total $129

## Slide 12
DRA-50M for VARA
Masters Communications DRA-50M
DRA-50M $115
DIN6 Cable $ 10
Yaesu CT-164 (Yaesu tax) $ 48
Total $173

## Slide 13
Common HT TNC for AX25
MobiLinkD TNC4
TNC4 $150
Radio Cable (FT-60) $ 10
Total $160

## Slide 14: WINLNK ON THE WEB
https://www.winlink.org
or simply
winlink.org

## Slide 15: Winlink.org

## Slide 23: Another important website
https://emcomm-training.org/Winlink_Thursdays.html

## Slide 24: Winlink Express application
Download from Winlink.org
Expand the ZIP file
Run as Administrator
Installs into C:/RMS Express
Run it
Agree to License Agreement
Previously known as:
Winlink 200 or RMS Express

## Slide 28: Creating a Winlink Message
From the Message Menu
Select New Message

## Slide 29: Message Types
Winlink Message
  Sent normally through an RMS Gateway
Radio Only Message
  Can only be sent/received over ham radio
Post Office Message
  Station stays online and receive messages
    Message sent to Post Office are kept
    Receiver must log in to retrieve
Peer-to-Peer Message
  Both stations are online
  One side connects (via callsign) to the other
    Once connected, messages are transferred

## Slide 30: Addressing messages
The “TO” field can either be a callsign or an Internet Address
An Internet Address is of the form <a>@<domain>
RECEIVING ADDRESSES
In order to limit SPAM, Winlink implements an ACCEPTLIST for Internet Addresses.
There are two ways to get an Internet Address in the ACCEPTLIST
1) send a Winlink email to that address
2) Edit the ACCEPTLIST on Winlink.org

## Slide 31
Symbol meanings can be found on the Winlink.org FAQ

## Slide 32: VARA FM
VARA FM (used for VHF/UHF)
available on the WinLink.org -> Download -> VARA Products page
Download and install as administrator
It’s worth it to pay for the software
One time fee
Cost is now US$75

## Slide 34
EUGENE AREA AX25 & VARA FM PACKET NODES
AX25 |  |  |  | 
 | Name | Frequency | {Digipeater} | Location
 | W7EUG-10 | 145.030MHz | WALKER (W7SLA-1) | Courthouse
VARA FM |  |  |  | 
 | Name | Frequency | {Digipeater} | Location
 | W7EUG-7 | 145.970MHz | W7FLO-1 W7FLO-9 | County Shops
 | W7EUG-8 | 145.970MHz | W7FLO-1 W7FLO-9 | Courthouse
Use the Digipeater (in the “via” field) if you can not “reach” node.

## Slide 35: Online documents
Copies of this presentation and list of URLS are available at:
https://eugeneemcomm.org/winlink/